## Slide 1: Lab Equipment

## Slide 2: Beaker
Holding liquids
• may be graduated (sometimes in two directions)
• has a white spot for labeling
• various sizes including 50, 150, 250, 450, 650, and 1000 mL

## Slide 3: Erlenmeyer Flask
Holding liquids
• shape avoids loss due to splashing
• used for titration
• common sizes include 125, 250, and
500 mL

## Slide 4: Florence Flask
Heating liquids
• shape allows even distribution of heat while boiling
• never graduated
•common sizes include 250 and 500 mL

## Slide 5: Test Tubes
Holding liquids or solids
• can be heated directly or in a water bath
• may be used to mix small quantities of
chemicals
• large variety of sizes

## Slide 6: Test Tube Brushes
Test tube brushes are used to clean test tubes and graduated cylinders.
Forcing a large brush into a small test tube will often break the tube.

## Slide 7: Test Tube Racks
Test tube racks are for holding and organizing test tubes on the laboratory counter. Plastic racks may melt in contact with very hot test tubes.

## Slide 8: Funnel
Funneling liquids
• useful for pouring liquids through small
openings
• can contain filter paper for separating
solids from suspensions by filtration

## Slide 9: Evaporating Dish
Evaporating solvent
• evaporation from a solution
• can be used to dry a damp product
• ceramic material allows direct heat to high
temperatures

## Slide 10: Watch Glass
Holding or covering
• useful for holding a sample of chemical
• may cover a beaker or flask to prevent
evaporation
• holds chemicals while drying

## Slide 11: Crucible
Heating to high temperatures
• heating covered or partially covered samples
• ceramic material may be directly heated
until red hot

## Slide 12: Pipe Stem Triangle
Providing a base to hold a crucible
• sits atop a wrought-iron ring
• stems are made of ceramic material

## Slide 13: Graduated Cylinder
Measuring volumes of liquids
• sizes vary
• commonly 10, 25, 50, 100, and 250 mL

## Slide 14: Burette
Measuring volumes of liquids
• delivers various volumes through a valve
called a stop cock
• more precise (exact) than the graduated
cylinder

## Slide 15: Mohr Pipet
A Mohr pipet measures and delivers exact volumes of liquids.

## Slide 16: Volumetric Pipette
Measuring volumes of liquids
• may be graduated
• may be volumetric (designed to deliver one
specific volume)
• liquid is drawn

## Slide 17: Thermometer
Measuring temperatures
• bulb should be submerged in the fluid being measured
• temperature ranges vary
• most contain dyed alcohol
• more precise thermometers contain mercury
• commonly measure temperature in degrees Celsius

## Slide 18: Ring stands and their Components
Ring stands are a safe and convenient way to perform reactions that require heating using a Bunsen burner.

## Slide 19: Ring stands and their Components Iron Rings
Iron rings connect to a ring stand and provide a stable, elevated platform for the reaction.

## Slide 20: Ring stands and their Components Utility Clamps
Utility clamps are used to secure test tubes, distillation columns, and burets to the ring stand.

## Slide 21: Ringstands and their Components Double Burret Clamps
Double Buret clamps are used to burets – long graduated tubes used in titration.

## Slide 22: Ring stands and their Components Wire Gauze
Wire gauze sits on the iron ring to provide a place to stand a beaker.
On older wire gauze, the white material is asbestos!

## Slide 23: Strikers
Strikers are used to light Bunsen burners.
The flints on strikers are expensive. Do not operate the striker repeatedly just to see the sparks!

## Slide 24: Bunsen Burner
Bunsen burners are used for the heating of nonvolatile liquids and solids.

## Slide 25: Test Tube Holder
A test tube holder is useful for holding a test tube which is too hot to handle.

## Slide 26: Beaker Tongs
Beaker tongs are used to move beakers containing hot liquids

## Slide 27: Crucible Tongs
For handling hot crucibles; also used to pick up other hot objects. NOT to be used for picking up beakers!

## Slide 28: Spatulas
Spatulas are used to dispense solid chemicals from their containers.
Chemicals should never be transferred with your bare hands!!!!!

## Slide 29: Volumetric Flask
A volumetric flask is used to make up a solution of fixed volume very accurately

## Slide 30: Gas Collecting Bottle
We use gas collecting bottles when large volumes of gases are produced, and must be collected by the displacement of water.

## Slide 31: Rubber Stoppers
Rubber stoppers are used to close containers to avoid spillage or contamination.
Containers should never be heated when there is a stopper in place.

## Slide 32: Spot Plates
Spot plates are used when we want to perform many small scale reactions at one time. We will use these many times during the year.

## Slide 33: Glass Stir Rod
A glass rod is used to manually stir solutions. It can also be used to transfer a single drop of a solution.

## Slide 34: Medicine Dropper
A medicine dropper is used to transfer a small volume of liquid (less than one mL).
On top of each medicine dropper is a “rubber bulb”

## Slide 35: Litmus Paper
Red litmus paper is used to identify bases.
Blue litmus paper is used to identify acids.

## Slide 36: Forceps/Tweezers
Forceps (or tweezers) are used to pick up small objects.

## Slide 37: Wash Bottle
A wash bottle has a spout that delivers a wash solution to a specific area. Distilled water is the only liquid that should be used in a wash bottle.

## Slide 38: Weighing Boat
Weighing boats are used to weigh solids that will be transferred to another vessel.

## Slide 39: Glass Plates
Glass plates provide a surface for semi-micro scale experiments, such as drop reactions and testing of acids and bases.

## Slide 40: Triangular File
Triangular files are used primarily to cut glass rod, a skill that your instructor will share with you when it becomes useful.

## Slide 41: Pressed Fiber Pad
A 4” x 4” square of ceramic fiber, it provides a surface for hot beakers so that the beaker does not come in contact with a cold countertop and shatter.

## Slide 42: HOMEWORK
1.1 Review Questions
(4, 5, 15)